## Slide 1: TRUSSES 1 P3 & P4

## Slide 2: Trusses – resolution of joints /graphical method
10kN
20kN
RA
RB
2m
2m
Find Reactions at A & B in usual way
( by taking moments about a reaction point and equating to zero)
RA = 12.5kN, RB = 17.5kN

## Slide 3: Joint A – consider forces
Draw to scale =12.5
Parallel to AC
Parallel to AE
A
C
D
E
B
Measure (to scale) the other two forces
Put on the direction of forces arrows and transfer to truss
AC –14.4kN ----strut (compression)
AE---7.2kN ------Tie (tension)
12.5kN
SPACE DIAGRAM
FORCE DIAGRAM
= 7.2 kN and 14.4 kN

## Slide 4: Joint C
A
C
D
E
B
CD---8.7kN ----strut (compression)
CE---2.8kN ------Tie (tension)
SPACE DIAGRAM
14.4kN
10.0kN
Parallel to AC & drawn to scale =14.4
External Force drawn to scale = 10
Parallel to CD from end of ext force
Parallel to CE from end of force in AC
Measure (to scale) the unknown forces
= 8.7 kN and 2.8 kN
Put on the direction of forces arrows and transfer to truss

## Slide 5: Subsequent Joints
Carry on joint by joint in a clockwise direction until all member forces known.
Resolution of forces Can be done by calculation alone

## Slide 6: Resolution of forces at joints
Consider Forces at Joint A: consider forces +ve up and to right
SV =0 gives,
12.5 + AC x Sin 60o = 0
AC = - 12.5/ Sin 60o
AC = -14.4 kN
( -ve means acts downwards)
Acts as a strut (compr.)
12.5kN
60o
Consider SH = 0
-AC x Cos 60o + AE = 0
AE = AC x Cos 60o
AE = 14.4 x 0.5
AE = 7.2 kN
Acts as Tie ( tension)
A
C
E
Sin() = Opp/Hyp
Opp = Hyp x Sin ()

## Slide 7: Resolution of forces at joints
Consider Forces at Joint C: consider forces +ve up and to right
10kN
60o
C
E
A
D
SV =0 gives,
AC x Sin 60o - 10.0 - CE x Sin 60o = 0
12.5 – 10 – CE (0.866) = 0
2.5 - CE (0.866) = 0
CE = 2.5/0.866
CE = 2.88 kN (acts in direction we presupposed)
Acts as a tie (tens.)
SH =0 gives,
CA x Cos 60o + CD + CE x Cos 60o = 0
14.4 (0.5) + CD + 2.88 (0.5) = 0
CD = - 7.2 -1.44
CD = -8.66 kN (opposite direction to what we thought)
Acts as a strut (compr)