## Slide 1: Abnormal coagulation results
Real or Fake?

## Slide 2: objectives
Discuss common preanalytical variables that may affect coagulation testing
Recognize analytical variables that may interfere with coagulation results
Correlate coagulation results with patient condition

## Slide 3: Lab detectives
Coagulation can be tricky and sometimes the unexpected happens
Coagulation samples are less forgiving than chemistry and hematology samples
Knowing what can effect coagulation assays is important
  Preanalytical and analytical phases of testing

## Slide 4: Preanalytical errors
All factors that may affect a patient specimen or sample analysis from the point of ordering to the point of analysis
Largest contribution (60-70%) to total laboratory error in the total testing process
Clotting assays are particularly susceptible due to complex enzymatic reactions
Sometimes divided into pre- preanalytical phase (test ordering) and preanalytical phase (from sample collection to analysis)

## Slide 5: Standards
International Council for Standardization in Haematology recommendations for processing of blood samples for coagulation testing
CLSI document H21 Collection, Transport and Processing of Blood Specimens for Testing Plasma Based Coagulation Assays and Molecular Hemostasis Assays
  5th ed.
  Published 2005

## Slide 6: Cost of errors
Cost of each preanalytical error ~ $200
$1.2 million for a 650 bed hospital
Around 5% of samples

## Slide 7: Analytical Errors
Those which occur during the testing phase
  Analyzer
  Reagent
  Sample
Does this make sense???

## Slide 9: Role of Vitamin k
Adds a binding site to
  Factors 2,7,9,10
  Protein C and S
Without binding site, factors are impaired
Vitamin K
  Diet
  Gut bacteria

## Slide 10: Sample collection
Coagulation samples should be collected with 19-21 gauge needle with good access
  22-23 gauge for children
Mixed gently 3-4 times
Tube should be 90% full
Catheter draws
  Heparin contamination

## Slide 11: UNDERFILLED AND OVERFILLED TUBES
3.2% Na citrate anticoagulant in ratio of 9 parts of whole blood to 1 part anticoagulant (9:1 ratio)
Requires 90% tube fill followed by 3-4 gentle inversions for mixing
Incorrect ratio of whole blood to citrate
  Under-filled (<90%): falsely prolonged
clotting times due to reduced calcium and dilutional effect
  High hematocrit (>55%) can have the same effect
  Over-filled: uncommon with vacuum tubes
but can occur with opened tubes/ syringe fills and result in falsely shortened clotting times

## Slide 12: Collection tubes
Different manufacturers
  Different plastic
  Different siliconized glass
  Composition of stoppers
  Difference in vacuum
All tube types must be validated

## Slide 14: Transport of fresh samples
Fresh samples should be transported to the laboratory promptly at ambient temperatures (18-24degrees C)
Transporting at colder temperatures or on ice is not recommended
  Cold precipitate of fibrinogen, factor 8 and vonWillebrand factor
  Cold activation of factor 7 and 12 which leads to a shortened PT and PTT
High temps degrade factors 5 and 8

## Slide 15: Sample ANALYSIS
Avoid storage of whole blood samples for coagulation testing at 2-8 º C prior to analysis
Time dependent loss of factor 8 and vonWillebrand factor
One study classified normal subjects as being misclassified as having vWD in 50% of samples stored at 2-8º prior to processing and analysis

## Slide 16: Clots in Citrated Samples
Coagulation process can be activated during collection and processing of samples
Leads to generation of activated clotting factors
Results in shortened clotting times
Fibrin clots are pale in color and may appear in the plasma after a freeze-thaw cycle
Partial clotting or activation may be difficult to detect
  ICSH recommends that any PTT results 4 or more seconds below lower limit of reference range should be recollected due to the possibility of partial clotting

## Slide 17: Centrifugation
Centrifugation should be sufficient to deliver platelet poor plasma
  Residual platelet count of <10,000
Platelets can interfere with certain testing
Platelets absorb unfractionated heparin out samples
Fresh samples can be tested after a single spin

## Slide 18: Sample stability
PT: stable for 24 if at room temperature and capped
  4 hours if uncapped
aPTT: stable for 4 hours at room temperature
  If heparinized, sample must be spun within 1 hour but run within 4 hours
Xa: unfractionated heparin, spun within 1 hour and run within 4
  Low molecular weight heparin: 24 hours
Fibrinogen and D-dimer: 4 hours at room temperature
Factor assays: 4 hours

## Slide 19: Centrifugation
If samples are to be frozen prior to testing, essential that a second spin be performed to remove any residual platelets
  Platelets rupture after freezing and release contents which can interfere with testing
Centrifuge the draw tube.
Take plasma layer off to an aliquot tube. Be careful not to disturb the platelet layer.
Centrifuge the First Aliquot tube.
Take off plasma leaving a small amount at the bottom of the tube. Use care not to aspirate the pellet of Platelets/RBC at the bottom of the tube.

## Slide 20: hemolysis
Cause of hemolysis
  Due to in vivo RBC disruption as a consequence of disease process
  In vitro lysis due to collection, transport, storage or processing
Visual checks can be operator dependent
Manufacturers are adding automated detection of hemolysis
Can interfere with optical measurement
Hemolysis can multi-factoral
  Clotting factor activation
Recommended to recollect hemolyzed samples

## Slide 21: Icterus and lipemia
Interferes with photo optical methods
Irrelevant in mechanical methods
Lipemic samples can be double spun using a high speed centrifuge to remove lipids
  Validated at each site prior to use

## Slide 22: Other interfering substances
Package inserts
CRP
Rheumatoid factor

## Slide 23: Secondary aliquots
Sodium citrate anticoagulant only
  No EDTA, Heparin or serum
Polypropylene aliquot tubes (translucent)
  tubes have double-walls to minimize evaporation, especially for
  coagulation-based tests: polypropylene inner surface to prevent surface activation and prevent anticoagulant evaporation, and outer polyethylene layer to prevent breakage during freezing or centrifugation
Do not use polysterene (transparent)

## Slide 24: Sample thawing
Frozen citrated plasma should not be allowed to thaw slowly at room temperature
  Precipitation of fibrinogen, factor 8, vWF and Antithrombin
Samples should be thawed in a 37º C waterbath for 5 minutes
  Mixed by gentle inversion 6-8 times
  Check for bubbles or fibrin clots

## Slide 25: Visual checks
Proper fill
Bubbles
Hemolysis/icterus/lipemia
Clots
High hematocrit

## Slide 26: Anticoagulants
Coumadin
Oral
Vitamin K antagonist
Half-life = ~3 days
Clearance = liver
K
K
K
K

## Slide 27: Anticoagulants
Heparin
Intravenously or Sub-q
Indirect irreversible inhibition of thrombin and Factor Xa through antithrombin
Half-life = 30-150 min
Clearance = renal

## Slide 28: Anticoagulants
Direct thrombin inhibitors
Direct Xa inhibitors
  Xarelto
  Eliquis

## Slide 29: Patient condition
Underlying condition
  Inflammatory conditions
  Undiagnosed liver disease
  Myeloproliferative disease or leukemia
Anticoagulant therapy
Herbal supplements
Estrogen supplements
Dietary
Other interfering substances

## Slide 30: Case #1
A 60 year old female presents to the Walk-In clinic with respiratory illness that has lasted 10 days
Lab work revealed
  Normal CBC, Chemistries, PT, PTT, PLT count
  Dimer >20 mg/L. (<0.5)
Cat scan revealed no PE or DVT
Antibiotic therapy initiated
Repeat dimer 2 weeks later
  >20 mg/L

## Slide 32: Fibrinolysis
Tissue Plasminogen Activator
  Tpa
Activates plasminogen to plasmin
Fibrin Degradation products
  D-Dimer

## Slide 33: D-DIMER
Demonstrates both generation of fibrin and plasmin
A negative predictor test
Most often used to rule out a DVT or PE
Easy and automated
Latex immuno-turbidometric assay

## Slide 34: Elevated Dimer levels
DVT or PE
Arterial Clot
Cardiovascular disease
Infection
Inflammation
Liver disease
Malignancy
Renal disease
Pregnancy
Excessive exercise
DIC
Aging

## Slide 35: Acute DIC
  Rapid consumption of factors leads to sudden bleeding
  Bleeding occurs at multiple sites
  Fibrin (microclots) are formed and can disrupt organ function
  Patients may have renal, liver or respiratory failure
  Purpura fulminans-skin necrosis due to the depletion of protein C

## Slide 36: D-Dimer Levels
If the Dimer is negative, it rules out DIC
If the Dimer level is moderately elevated -1.0-4.0 mg/L FEU, DIC is unlikely
If the Dimer level is in the range of 8.0-10.0 mg/L or more, DIC is increasingly likely

## Slide 37: D-Dimer
Limitations
  Cloudy plasma may cause false negative results
  Presence of rheumatoid factor may cause false positives
  Hemolysis, icterus may interfere

## Slide 38: Case study 2
A 40 year old woman is set to have a hysterectomy so the physician orders pre op labs
PT = 48 sec INR = >5.0
PTT = 34 sec (24-35)
Fibrinogen = 350 mg/dL
Patient is not on any anticoagulants
No other medications
No bleeding with prior surgeries or childbirth

## Slide 39: Case Study 2
Possibilities
Sample
  Processing
Transport
Anticoagulants
Instrument
Patient condition

## Slide 40: Case study 2
Patient referred to Hematology to figure out cause of prolonged PT
Repeat PTINR = >5.0
Mixing study= indicated factor deficiency
  7 = 25%
  10 = 30%
  5 = 90%
  2 = 40%

## Slide 41: Case Study 2
Patient was diagnosed with an acquired Vitamin K deficiency
Patient stated that she had been diagnosed with malabsorption issues
Vitamin K not being absorbed in the gut

## Slide 42: Case study 3
A 15 year old female presents to her physician with heavy periods
PT = 60 sec INR 6.1
PTT = 70 sec
Fibrinogen 60
Dimer = .30
Patient otherwise healthy
No family history of bleeding disorders
Sample was drawn at another facility and frozen

## Slide 43: Case study 3
Possibilities
  Sample
  Processing
  Transport
  Patient condition
  Anticoagulants
  Instrument

## Slide 44: Case study 3
Tested another aliquot
Results were all normal

## Slide 45: Case study 4
A 74 year old female who has been in the hospital for 1 week starts to have bleeding issues so the physician orders lab work
PT = 13.5
PTT = 90
Fibrinogen = 300
Not on any anticoagulants
History of chronic kidney disease

## Slide 46: Case study 4
Results consistent with an acquired factor inhibitor or a non specific inhibitor
Further studies revealed what appeared to be a non specific factor inhibitor
  Rule out anticoagulant contamination

## Slide 47: Case study 4
Doctor insisted the patient was not on any anticoagulant
Heparin Xa level = 0.3. (0.3-0.7) ???????
Patient was receiving some sub cutaneous heparin to prevent clotting due to being bed ridden
  Very small amount, should not interfere with coagulation results
Sample was drawn via veinapuncture
Transported and processed correctly

## Slide 48: Case study 4
Patient was admitted with kidney failure
  Cre = 2.5
Heparin is cleared by the kidneys

## Slide 49: Case study 5
A 8 year old child has a family history of thrombosis so the physician orders some labs to see if they are at risk. The child had not had a thrombotic event
PT = 14.0. (12.0-14.5)
PTT = 28 (24-35)
Fibrinogen = 375 (200-450)
AT = 9%. (83-150%)
  Lower linearity of test
AT are only run on certain days, so sample was frozen

## Slide 50: Case study 5
Patient was diagnosed with AT deficiency
1 month later, another sample was drawn to recheck AT level
AT = 103%
Not being treated

## Slide 51: Case study 5
Possibilities
  Sample
  Transport
  Processing
  Patient condition

## Slide 52: Case study 5
Looked back at other AT that were performed that day
Determined that there were bubbles in the tube

## Slide 53: Case 6
A 37 year old male presents to the physician with a complaint of recent bruising episodes. Doctor orders routine blood work and a vonWillebrand panel
PT = 14.7 (12.0-14.5)
PTT= 40 (24-35)
Fibrinogen = 249 (200-450)
Dimer = 0.27 (<0.5)

## Slide 54: Case 6
Technologist noticed the hematocrit seemed high
  63.4 %

## Slide 55: Case 6
CORRECTION FOR HIGH HEMATOCRIT
Often needed in patients with cyanotic heart disease or polycythemia vera
When hematocrit > 55%, plasma volume/ citrate volume is decreased, leading to an anticoagulant effect of the excess citrate (reduced calcium with dilutional component)

## Slide 56: Case 6
• Citrate volume correction required:
Formula in CLSI guidelines H21-A5: c = (1.85 x 103)*(100-HCT)*(Vblood) Where: -c is the volume of citrate remaining in the tube (mL) -HCT is the hematocrit of the patient (%)
-Vblood is the volume of blood added (mL) - 1.85 x 103 is constant
Acceptable to remove 100 µL sodium citrate for HCT between 55-65%
  3 mL tube

## Slide 57: Case 6
Patient redrawn in a corrected tube
PT = 14.5 (14.7)
PTT = 36.0 (40)
Fibrinogen = 275 (249)
Dimer = 0.27 (0.29)

## Slide 58: conclusion
Labs should have good policies regarding collection, processing, transport, etc for coagulation samples
Be aware of policies
Does this make sense???

## Slide 59: References
Keohane, E. M., Walenga, J. M., & Otto, C. N. (2020). Chapter 35. In Rodak's hematology: Clinical principles and applications (pp. 637–643). essay, Elsevier.
Kitchen, S., Adcock, D. M., Dauer, R., Kristoffersen, A. H., Lippi, G., Mackie, I., Marlar, R. A., & Nair, S. (2021). International Council for Standardisation in Haematology (ICSH) recommendations for collection of blood samples for coagulation testing. International Journal of Laboratory Hematology, 43(4), 571–580. https://doi.org/10.1111/ijlh.13584
Seheult J, MB BCh BAO, MSc, MS, MD. 2021, October 6. “UNDERSTANDING PREANALYTICAL VARIABLES IN THE COAGULATION LABORATORY A CASE-BASED APPROACH “. Mayo Clinic Labs Bleeding and Thrombosing Diseases Conference and Workshop
Kottke-Marchant, K. (2016). Specimen Collection and Processing. In An algorithmic approach to hemostasis testing (pp. 43–54). essay, CAP Press.

## Slide 60
This Photo by Unknown Author is licensed under CC BY-NC-ND