# Text boxes

### Instructions

- 1. Adjust the position of your 3” X 5” tool rest so the
    top surface is level and the edge facing the wheel
    is within 1/8” of the wheel surface.

- 2. Tighten the cam lever and adjustment handle
    securely!

- 3. File or sand the edge of the platform rest facing
    you until it is smooth. Slightly chamfering the top
    edge is advisable.

- 4. Remove the rubber cap to expose the
    diamond tip.

- 5. Loosen the nylon knurled ring nut slightly.

- 6. Turn the round adjustment knob counter-
    clockwise to retract the position of the diamond
    close to the body.

- 7. Without the grinder running: Place the body of the
   dresser onto the top surface of your tool rest and
   slide the Tru-N-Dress across the wheel and adjust
   the position of the diamond until it very slightly
   contacts the wheel.

- 8. Move the diamond away from the wheel.

- 9. Put on a dust mask and a face shield and turn the
    grinder on.

- 10. Slide the Tru-N-Dress across the wheel with a
      smooth traverse, back and forth about 6 times.

- 11. Advance the position of the diamond very
      slightly by turning the adjustment knob.

- 12. Repeat step 10 and 11 a few times. Turn the
      grinder off and inspect the wheel. When the
      entire surface has been trued, move the tool rest
      to the other wheel and repeat the procedure.

- Call 352-472-5035 if you have any questions!

- Remember: Good sharpening begins with properly dressed wheels!

Tool rest

When truing the wheel, make light cuts and traverse across the wheel 6 to 8 times between adjustments.

Smooth and slightly chamfer this edge.

wheel

Make sure the tool rest is within 1/8” of the grinding wheel.

## Tool rest

Set the angle of your tool rest so it points toward the axle of the grinder or slightly downward.