Blade 150 SX

4 Stroke, OHV, Forced Air Cooled, Single cylinder,
Displacement: 150 cc (9.15 cu in)
Transmission: Automatic CVT with reverse
Ignition mode: CDI
Carburetor: 24mm cv
12hp/7500rpm
Bore & Stroke: 57.4 mm x 57.8 mm
Maximum Torque: 9.5/5500 Nm/r/min
Top Speed: approximately 35mph (depending on terrain and occupancy)
Gas Tank: 1.8 Gallons
Lubrication: Force & Splash

- Key switch with electric start

- Hydraulic front and rear disc brakes

- Rack and Pinion steering

- Dual A-Arm adjustable suspension

- Trailer hitch

- Individual adjustable racing style seats

- Dry Weight 362 LBS

- Body dimensions 84.5" x 51.2" x 57"

- 21”front and 22” rear aggressive off road tires

- Wheelbase 59"

- Chrome rims

- Ground clearance 6.7"

- Front suspension travel 6"

- Rear suspension travel 6"

- Double row chain with guard

- Foam padded roll cage

- Removable roof made of Ballistic Nylon

- Parking brake

- Speedometer, Gas gauge and 12 volt outlet, Horn

- Rear cargo rack

- Headlights

- Brake lights

- Tail lights

- Colors: Molten Red & Midnight Black